## Slide 1
CPU Microarchitecture Evaluation of Agentic AI Workloads
SimPoint-based trace collection & Scarab simulation
for LangChain, LangGraph, AutoGen, Haystack (RAG), and SWE-Agent
Surim Oh | April 2026

## Slide 2
Motivation
Agentic AI is an emerging CPU workload class — orchestration, tool calling, state management
Current CPU benchmarks (SPEC, GeekBench) don't capture agent execution patterns
Agent workloads have distinct microarchitectural signatures:
  Frontend-bound: deep call stacks, polymorphic dispatch, large code footprints
  Backend-bound: JSON/string processing, hash table lookups, dict manipulation
  Branch-heavy: conditional tool selection, state-machine transitions
Goal: characterize 5 agent workloads spanning frameworks and application archetypes
Method: perf stat (real HW) + SimPoint traces → Scarab cycle-accurate simulation

## Slide 3
Workload Suite Overview
Workload | Framework | Archetype | Key Computation | Mock Components | Peak RSS
LangChain | LangChain Core | Simple agent loop | JSON ser/deser, string ops | Fake tool (local_search) | 50 MB
LangGraph | LangGraph | ReAct agent (graph) | JSON, message passing, graph traversal | FakeToolCallingModel, 3 tools | ~80 MB
AutoGen | AutoGen AgentChat | Multi-agent (async) | Async orchestration, JSON, dict ops | ReplayChatCompletionClient | ~90 MB
Haystack | Sentence-Transformers + FAISS | RAG pipeline | FP32 embedding, SIMD dot-product, numpy matrix ops | Real model, synthetic corpus | 519 MB
SWE-Agent | LangGraph StateGraph | Multi-step planning agent | Regex, string/dict manipulation, branchy control flow | 6 mock dev tools, scripted 20-step sequence | 252 MB

## Slide 4
Workload Algorithms (1/3): LangChain & LangGraph
LangChain — Simple Agent Loop
Pipeline: plan → select_tool → marshal_request → invoke_tool → parse_response → synthesize
Single tool (local_search) returns deterministic JSON results
Context blob scales with --context-size: 416B (short) / 1.6KB (med) / 6.6KB (long)
Computational core: JSON encode/decode with sort_keys, dict operations
LangGraph — Graph-Structured ReAct Agent
Uses create_react_agent with FakeToolCallingModel
Per iteration: 3 tool calls (cpu_analyze → memory_profile → branch_analyze)
Adds message accumulation and graph-node traversal overhead
More framework overhead than LangChain: state checkpointing, edge routing

## Slide 5
Workload Algorithms (2/3): AutoGen & Haystack
AutoGen — Async Multi-Agent Framework
AssistantAgent with ReplayChatCompletionClient (7 scripted responses)
3 async tools: topdown_analyze, cache_profile, branch_stats
Python asyncio event loop adds coroutine scheduling overhead
Distinct from LangChain/LangGraph: async/await dispatch, different runtime path
Haystack — RAG Pipeline (Real ML Inference)
Real SentenceTransformer model: all-MiniLM-L6-v2 (22M params, FP32)
Pipeline: embed_query → FAISS vector_search (top-k=10) → rerank → synthesize
Corpus scales: 100 docs (short) / 500 (med) / 2000 (long)
SIMD-heavy: PyTorch FP32 inference, FAISS IndexFlatIP dot products, numpy ops
Only workload with real ML compute — expected backend-bound (memory/FP)

## Slide 6
Workload Algorithms (3/3): SWE-Agent
SWE-Agent — Multi-Step Planning Agent (Bug-Fix Simulation)
Built on LangGraph StateGraph with 5 nodes: planner → tool_selector → tool_executor → observer → check_done
Rich AgentState: task, plan[], completed[], file_state{}, observations[], step_count, messages
6 mock developer tools (pure-CPU, in-memory file system):
  read_file, write_file, list_dir — dict key/value operations
  grep_files — regex compilation + search across file corpus
  run_tests — conditional pass/fail based on step count
  apply_patch — deterministic string mutation (simulates a-b → a+b fix)
20-step scripted sequence per iteration with conditional replanning every 2 steps
Deepest control flow of all workloads — closest to real multi-step agent planning

## Slide 7
CPU Performance Characteristics (perf stat, Top-Down L1)
Framework | Retiring % | Bad Spec % | Frontend Bound % | Backend Bound % | Exec Time (representative) | Peak RSS
LangChain | 19.0 | 4.2 | 26.6 | 50.2 | 12s (short/250) | 50 MB
LangGraph | 17.9 | 4.1 | 30.8 | 47.2 | ~2 min | ~80 MB
AutoGen | 19.5 | 4.6 | 32.2 | 43.7 | ~2 min | ~90 MB
Haystack | 22.1 | 4.9 | 28.6 | 44.5 | 2m31s (short/100) | 519 MB
SWE-Agent | 19.9 | 4.5 | 26.7 | 48.9 | 2m8s (short/150) | 252 MB
All agent workloads are dominated by backend-bound stalls (44-53%) — memory/data dependencies
Frontend-bound is significant (25-32%) — large Python code footprint, indirect dispatch
Retiring is low (17-22%) — typical of interpreted languages with high overhead
Bad speculation is modest (4-5%) — branch prediction handles Python's patterns reasonably
Haystack shows higher variance across variants — real ML inference vs framework overhead

## Slide 8
Top-Down L1 Breakdown by Workload (Average Across Variants)
0%
25%
50%
75%
100%
19%
27%
50%
LangChain
18%
31%
47%
LangGraph
19%
32%
44%
AutoGen
22%
29%
44%
Haystack
20%
27%
49%
SWE-Agent
Retiring
Bad Speculation
Frontend Bound
Backend Bound

## Slide 9
Infrastructure Updates: scarab-infra
Added 5 agent workloads with Docker-containerized environments:
  LangChain, LangGraph, AutoGen — Python 3.10 + framework packages
  Haystack — sentence-transformers + FAISS + numpy (model pre-downloaded at build time)
  SWE-Agent — LangGraph StateGraph with rich state and 6 mock developer tools
Each workload: 6 variants (short/medium/long × 2 iteration counts) = 30 configurations
Trace pipeline: cluster_then_trace (SimPoint) with libfpg.so fingerprinting
Perf pipeline: perf stat with Top-Down L1 counters on pinned core
Slurm integration: parallel job submission, auto image build on nodes
Status tracking: ./sci --status shows per-job stage (fingerprinting/clustering/tracing/...)
Key files modified:
  workloads/agent/ — Dockerfile + run scripts (run_langchain.py, run_langgraph.py, etc.)
  json/agent_trace.json, agent_perf.json — 30-variant descriptors
  common/scripts/run_simpoint_trace.py — multi-thread handling, DR config isolation
  scripts/slurm_runner.py — stage progress, kill wait, image cleanup

## Slide 10
DynamoRIO Fixes (fork: 5surim/dynamorio)
Two problems with DynamoRIO on multi-threaded Python workloads
Root Cause 1: SIGSEGV crash — race in module_list_remove() (core/module_list.c)
  module_list_remove() released write lock for client callback, module still in vmvector
  Another thread gets module name pointer via vmvector_lookup during this window
  First thread re-acquires lock, frees module data → second thread's pointer is stale → SIGSEGV
Root Cause 2: libfpg.so not loading — DR config cross-contamination on shared NFS
  DR caches per-process configs in ~/.dynamorio/ keyed by binary+PID
  Concurrent slurm jobs on same NFS home pick up each other's config files
  Wrong config → libfpg.so client not loaded → empty fingerprint output
Fix 1 (for RC1): Root cause fix in module_list_remove() (core/module_list.c)
  Move module_area_delete() + vmvector removal before releasing write lock
  Client callback only uses client_data (a copy), does not need original module_area_t
  Eliminates the race window entirely — no thread can get a stale pointer
Fix 2 (for RC1): strhash_key_cmp safe_read guard (core/hashtable.c)
  Defense-in-depth: safe_read check on hash table key pointers before strcmp
Fix 3 (for RC2): Per-job HOME override (scarab-infra, run_simpoint_trace.py)
  HOME={workload_dir} on drrun commands — isolates ~/.dynamorio/ per job

## Slide 11
Scarab Fix + Multi-Threaded Workload Handling
Scarab Build Fix
GCC 11 (Ubuntu 22.04) treats -Wclass-memaccess as error with -Werror
cbp_tagescl_64k.h: memset() on non-trivial C++ classes (cbp64_folded_history, cbp64_lentry)
Fix: replaced memset with default-construction loops:
  for (auto &x : ch_i) x = cbp64_folded_history();
  for (auto &row : ch_t) for (auto &x : row) x = cbp64_folded_history(); // 2D array
  for (auto &x : ltable) x = cbp64_lentry();
Multi-Threaded Fingerprint Handling
Python workloads spawn helper threads (GC, import, signal handlers)
libfpg.so creates per-thread fingerprint files (bbfp.<thread_id>)
cluster_then_trace expected exactly 1 bbfp file — failed with multiple
Fix: pick the main thread's fingerprint (file with most segments)
CPython GIL ensures main thread dominates instruction execution
Simulating the dominant thread on a single core is representative

## Slide 12
Current Status
Component | Status | Details
Perf collection (perf stat) | Complete | 30/30 variants collected Top-Down L1 data in workloads_db.json
Trace collection (SimPoint fingerprint) | In progress | 30 jobs running on slurm cluster (cluster_then_trace mode with libfpg.so)
Trace collection (SimPoint clustering + tracing) | Pending | Runs after fingerprinting completes
Scarab simulation | Pending | Will run after traces are collected
DynamoRIO fork | Fixed | Root cause fix in module_list_remove() + strhash_key_cmp guard + HOME isolation
Scarab fork | Fixed | GCC 11 build fix for cbp_tagescl_64k.h

## Slide 13
Next Steps (1/2): Trace Collection & Analysis
1. Complete SimPoint trace collection (30 workload variants)
  Fingerprinting → clustering → representative segment tracing
  Expected: ~10-20 simpoints per workload variant
2. Run Scarab cycle-accurate simulation on collected traces
  Simulate each simpoint segment with detailed microarchitecture model
  Collect IPC, cache miss rates, branch misprediction rates, pipeline utilization
3. Detailed microarchitectural analysis
  Compare agent workloads vs traditional benchmarks (SPEC, datacenter)
  Identify bottlenecks: i-cache misses, d-cache pressure, branch misprediction
  Characterize per-workload signatures: RAG (backend/SIMD) vs framework (frontend)
4. Control flow graph (CFG) analysis
  Extract CFGs from traces: basic block size distribution, branch type breakdown
  Compare loop depth, fan-out, indirect branch density across workloads
  Hot code footprint: what fraction of unique PCs covers 90%/99% of execution?

## Slide 14
Next Steps (2/2): Architecture Sensitivity Studies
5. Frontend-bound studies
  I-cache size sweep (32/64/128KB) — Python's large code footprint likely causes high i-miss
  BTB size sensitivity — many indirect branch targets from polymorphic dispatch
  Fetch/decode width sensitivity — wider frontend vs capacity-bound?
6. Backend-bound studies
  D-cache hierarchy sweep: L1D (32/48/64KB), L2 (256/512KB/1MB), LLC (2/4/8MB)
  Reuse distance analysis — quantify temporal locality in dict/JSON/hash table accesses
  ROB size sensitivity (256/384/512) — larger ROB to extract MLP and hide cache misses
  Prefetcher effectiveness — stride vs complex; irregular access patterns may defeat stride
7. Cross-cutting studies
  Core width sweep (4/6/8-wide) — are agent workloads ILP-limited?
  Branch predictor config sweep — TAGE history length, indirect predictor sizing
  Haystack (FP/SIMD) vs framework (branchy/string) — quantify architectural divergence
8. Upstream DynamoRIO fix
  Submit PR with module_list_remove() race fix to DynamoRIO upstream

## Slide 15
Appendix: SimPoint Methodology (cluster_then_trace)
Phase 1: Fingerprinting
  Run workload under DynamoRIO with libfpg.so client
  Collect basic block frequency vectors every 10M instructions (segment)
  Output: bbfp.<tid> (fingerprint) + pcmap.<tid> (PC mapping)
Phase 2: Clustering
  SimPoint k-means clustering on BB frequency vectors
  Select representative segments (simpoints) with weights
  Typically 10-20 clusters per workload
Phase 3: Trace Collection
  Re-run workload under DynamoRIO drcachesim, trace only selected segments
  -trace_after_instrs N -trace_for_instrs M to capture specific instruction windows
  5 segments of warmup (50M instructions) before each simpoint
Phase 4: Simulation (next step)
  Feed traces to Scarab cycle-accurate simulator
  Weighted IPC = sum(simpoint_weight × simpoint_IPC)